## Slide 1: 2025 International Conference on Smart & Sustainable Technology (INCSST) Hosted By : K. L. E. College of Engineering & Technology , Chikkodi , Karnataka , India
Real-Time Mobile Phone Usage Detection and Automated Ticketing Using YOLO Deep Learning Algorithm
Paper ID: 465
M.VAMSI KRISHNA : 21691A04Q9
P.VENU KUMAR : 21691A04R9
M.VISHNUVARDHAN : 21691A04T0
Affiliation
Department of ECE,
Madanapalle Institute of Technology & Science (MITS),
Madanapalle, Andhra Pradesh, India

## Slide 2: Introduction
This project detects mobile phone usage by two-wheeler riders in real-time.
It uses the YOLO deep learning model and a Raspberry Pi for processing.
A USB webcam captures live video of the riders.
YOLO analyzes the video to check if a rider is using a mobile phone.
If a violation is found, the number plate is read using Tesseract OCR.
An LCD screen displays the detected information.
The system helps improve road safety by detecting and reporting violations automatically

## Slide 3: Problem Statement & Objectives
Problem Statement: Existing traffic monitoring systems fail to automatically detect and penalize two-wheeler riders using mobile phones.
Project Objectives:
Detect mobile phone usage by two-wheeler riders using YOLOv8.
Identify and extract the vehicle number plate using OCR.
Send an automated email with ticket and evidence to the violator.

## Slide 4: Proposed System Overview
Main Modules:
Camera: Captures real-time images of two-wheeler riders.
YOLOv8: Detects mobile usage, rider, number plate, and vehicle.
OCR (Tesseract): Extracts text from number plates.
Email System: Sends violation details to registered email.
LCD Display: Shows system status and alerts.
Camera
YOLOv8 Detection
OCR
Email Module
LCD Display

## Slide 5: YOLOv8 Model Explanation
YOLO (You Only Look Once) is a state-of-the-art, real-time object detection algorithm.
YOLOv8 Features:
  Fast and accurate detection
  Single forward pass: real-time capable
  Suitable for edge devices like Raspberry Pi
Custom Classes Trained:
Rider
Mobile phone
Number Plate
Two-wheeler

## Slide 6: Dataset & Model Training
Dataset Preparation:
1100+ real-world images collected manually
Labeled using Roboflow
Training Details:
Trained on window powershell using YOLOv8
Image size: 640x640
Epochs: 100
Precision: 91.3%, Recall: 88.5%, mAP: 90%
Visuals:
Confusion matrix
Precision-recall curve
Training loss graphs

## Slide 7: Hardware & Software Used
Hardware:
Raspberry Pi 4B
USB Camera (1080p)
LCD Display (16x2 or TFT)
12V Adapter, Power Supply
GPIO for alerts
Software:
Python 3.10
YOLOv8 (Ultralytics)
OpenCV
Tesseract
SMTP for emails
Roboflow for labeling

## Slide 8: System Workflow / Algorithm
Capture frame using USB camera.
Run YOLOv8 detection on frame.
Apply OCR on cropped number plate.
Store detection image + text result.
Send automated ticket via email.
Show alert on LCD display.
Mobile
rider
two-wheeler
crop number plate region

## Slide 9: Detection Results
Object Tracking Output Using DeepSORT for Consistent Rider Identification

## Slide 10
Normalized confusion matrices for multi-class classification of riders, mobile phone users, and license plates.
Training and validation loss and metric trends for the YOLOv8 model over 100 epochs.
Outputs Graphs

## Slide 11: Number Plate Recognition Using Tesseract OCR

## Slide 12
F1 score and precision vs. confidence curves for YOLOv8 multi-class detection performance.
Recall-confidence and precision-recall curves depicting model detection quality.
Outputs Graphs

## Slide 13: Automated Ticketing Email
Email Components:
Subject: "Traffic Violation Alert"
Body:
  Rider detected using mobile phone
  Number Plate: AP02BG7653
  Date & Time: 12-05-2025 | 12:35 PM
Attachment: Violation image (JPG/PNG)
SMTP Email Code: Python smtplib used to send email securely.
Output Email:

## Slide 14: Conclusion&Future Scope
Conclusion:
Successfully implemented real-time detection system.
Automatically captures, identifies, and reports mobile usage by two-wheeler riders.
Effective solution for smart traffic enforcement.
Future Scope:
Integration with RTO database for direct challan issuance.
Helmet detection
Web dashboard for traffic departments
Multilingual OCR support

## Slide 15: References
1. Redmon, J., Divvala, S., Girshick, R., & Farhadi, A. (2016). *You Only Look Once: Unified, Real-Time Object Detection*. In Proceedings of the IEEE Conference on Computer Vision and Pattern Recognition (CVPR), 779-788.
2. Zhang, Y., & Xie, L. (2019). *Real-time Object Detection for Mobile Applications Using YOLO*. International Journal of Computer Science and Information Security, 17(4), 23-29.
3. Kumar, A., & Singh, V. (2021). *Mobile Phone Detection for Traffic Safety Using Machine Learning*. Journal of Traffic Safety and Technology, 34(2), 123-132.
Acknowledgements:
Dr. C. Kumar (Guide)
ECE Department, MITS
M.VAMSI KRISHNA : 21691A04Q9
P.VENU KUMAR : 21691A04R9
M.VISHNUVARDHAN : 21691A04T0
Open-source communities (Ultralytics, OpenCV, Roboflow, etc.)